## Slide 1: Project: Collective Optimization for Cross Region AI Acceleration (COCA) Updates on PoliMi’s Activities (Dec.18.2024-Feb.4.2025)
Qiaolun Zhang, Jiaheng Xiong, Xiaomin Liu, Hessam Hashemizadeh, Nicola Di Cicco,
Mëmëdhe Ibrahimi, Francesco Musumeci , Massimo Tornatore
February 4th, 2024

## Slide 2: Outline
Local-Topology-Aware CCL (LTCCL)
  Motivation
  Problem Statement
  Heuristic Algorithm
  Results (Comparison with TECCL)

## Slide 3: Motivation: Limitation of Previous Approaches
Previous approach: transmit multiple chunks together to reduce propagation delay
“𝛼 − 𝛽” cost model
  𝛼: fixed delay over a link (propagation, processing)
  𝛽: transmission delay associated with sending 1 bit of data over a link (1/capacity)
Existing works do not investigate choice of chunk size

## Slide 4: Motivation: Dividing Chunks to Sub-Chunks
TECCL is too slow to solve multi sub_chunks problem
TECCL cannot accurately model propagation delay
Transmit entire chunk
𝛼
𝛽
𝛽
𝛼
Transmit chunk divided to 2 sub-chunks
𝛼
𝛽/2
𝛽
𝛼
2 hops: Dividing a chunk into k sub-chunks  reduces delay by 𝛽
2𝛼 + 2𝛽 vs. 2𝛼 + 2/3𝛽
GPU 1
GPU 2
GPU 3
GPU 1
GPU 2
GPU 3
Transmit chunk divided to 2 sub-chunks
Node 1
Node 2
Node 3

## Slide 5: Problem Statement
Problem statement
Given
Decide
Objective
Constraints
Network topology of multiple data centers
Collective operation
Chunk size
Number of subchunks
Routing of chunks
Scheduling of forwarding chunks in one node
Minimize the required to finish the collective
Link latency
Node can only send a packet after receiving it
Each chunk can be split into multiple sub-chunks
Notes: multicast in a big topic

## Slide 6: Issue of Epoch Duration in TECCL
Epoch
  Fast link case: epoch is defined as the delay of one chunk over the fastest link
  Slow link case: epoch is defined as the delay of one chunk over the slowest link
Fast link case: finer-grained schedules
When propagation delay + transmission delay > one epoch duration:
  E.g., 1 second + 0.1 second > 1 second  2 epochs used, 0.9 second wasted
𝛼 = 0.1 s
𝛽 = 1 s
𝛽 = 1 s
𝛼 = 0.1 s
2 epochs = 2s
GPU 1
GPU 2
GPU 3

## Slide 7: Choice of Epoch/Timestep
Impact of epoch:
  If epoch is too small, running time is too long
  If epoch is too big, the performance is poor
A smaller epoch than TECCL
  For all link rates, calculate
  Find their greatest common divisor (GCD) for all R and propagation delays
  Set epoch as the GCD
Example
  Link capacity = [25, 50] Gb/s, propagation delay = [0.000015, 0.00005]s, chunk size = 1Gb
  R = [0.04, 0.02]s, GCD(0.004, 0.002, 0.000015, 0.00005) = 0.00005
  Epoch is set to: 0.00005s

## Slide 8: Flow Chart of the Proposed Algorithm
Collective finished
Decide nodes that not need broadcast
Divide chunks into sub-chunks
GPU0
GPU1
GPU0
GPU2
GPU1
GPU2
Finish Time with sub-chunks
Finish Time
without sub-chunks
Start Time
Each chunk will be divided into multiple sub-chunks, and independent decisions will be made for each sub-chunk
Packet sorting
Next Event
No
Yes

## Slide 9: Flow Chart: Prevent Redundant Transmission
GPU2
GPU1
GPU3
GPU4
GPU0
0
0
0
0
0
GPU1
GPU3
GPU0
0
0
0
0
0
0
GPU2
GPU4
Each node broadcasts the chunks it already possesses to the neighboring nodes
        Prevent redundant transmission to nodes already having the chunk
Collective finished
Decide nodes that not need broadcast
Divide chunks into sub-chunks
Packet sorting
Next Event
No

## Slide 10: Flow Chart: Packet Sorting
If multiple nodes plan to send the same chunk to one node:
  Select the node that can send this chunk fastest considering
    Sending queue
    Link rate
GPU2
GPU1
GPU3
GPU4
GPU0
0
0
0
0
1
2
3
0
GPU2
GPU1
GPU3
GPU4
GPU0
0
0
0
0
0
0
0
The packet plan to send
The packet is sending in the link
Low speed link
Hight speed link
Collective finished
Decide nodes that not need broadcast
Divide chunks into sub-chunks
Packet sorting
Next Event
No

## Slide 11: Detailed issues
For the links between different chassis, we prefer to select different chunks transmit in these links at the same time
Chassis 1
Chassis 0
1
2
3
1
2
3
1
2
3
1
2
3
The transmission within the chassis is fast, and the performance bottleneck lies in the link between chassis connections.
This design will usage the transmission time in links between chassis to finish broadcast inner chassis

## Slide 12: Initial Result: Topology
DGX topology with 1 chassis
NDv topology with 4 chassis

## Slide 13: Collective time(Allgather, one datacenter)
Unit: | NDv2, 1 chassis |  | NDv2,2 chassis |  | NDv2, 3 chassis | 
 | TECCL | LTCCL | TECCL | LTCCL | TECCL | LTCCL
1MB | 97.65 | 78.825 | 742.18 | 686.29375 | 1386.72 | 1390.71875
4MB | 390.62 | 313.2 | 2968.75 | 2737.075 | 5546.86 | 5550.875
16MB | 1562.5 | 1250.7 | 11875 | 10940.2 | 22187.5 | 22191.5
64MB | 6250 | 5000.7 | 47500 | 43752.7 | 88750 | 88754
256MB | 25000 | 20000.7 | 190000 | 175002.7 | 355000 | 355004
 | NDv2, 1 chassis |  | NDv2,2 chassis |  | NDv2, 3 chassis | 
 | TECCL | LTCCL | TECCL | LTCCL | TECCL | LTCCL
1MB | 97.65 | 78.825 | 742.18 | 686.29375 | 1386.72 | 1390.71875
4MB | 390.62 | 313.2 | 2968.75 | 2737.075 | 5546.86 | 5550.875
16MB | 1562.5 | 1250.7 | 11875 | 10940.2 | 22187.5 | 22191.5
64MB | 6250 | 5000.7 | 47500 | 43752.7 | 88750 | 88754
256MB | 25000 | 20000.7 | 190000 | 175002.7 | 355000 | 355004
LTCCL is better than TECCL when topology is small (num_chunk is 1)

## Slide 14: Execution time(Allgather, one datacenter)
Polling will bring long execution time
Event driven method significantly reduce the execution time
Unit: | NDv2, 1 chassis |  |  | NDv2,2 chassis |  |  | NDv2, 3 chassis |  | 
 | TECCL | LTCCL |  | TECCL | LTCCL |  | TECCL | LTCCL | 
 |  | old | new |  | old | new |  | old | new
1MB | 0.15 | 4.41 | 0.002290 | 15.77 | 208.81 | 0.027781 | 281.17 | 637.14 | 0.085879
4MB | 0.15 | 4.20 | 0.002129 | 15.85 | 221.5 | 0.027658 | 279.27 | 635.8 | 0.091433
16MB | 0.15 | 4.27 | 0.002116 | 16.19 | 176.18 | 0.027027 | 294.68 | 644.48 | 0.086973
64MB | 0.15 | 4.36 | 0.002137 | 17.83 | 238.83 | 0.027488 | 281.28 | 642.91 | 0.086046
256MB | 0.15 | 19.07 | 0.002112 | 18.82 | 912.81 | 0.027972 | 292.88 | 2448.83 | 0.086941
 | NDv2, 1 chassis |  |  | NDv2,2 chassis |  |  | NDv2, 3 chassis |  | 
 | TECCL | LTCCL |  | TECCL | LTCCL |  | TECCL | LTCCL | 
 |  | old | new |  | old | new |  | old | new
1MB | 0.15 | 4.41 | 0.002290 | 15.77 | 208.81 | 0.027781 | 281.17 | 637.14 | 0.085879
4MB | 0.15 | 4.20 | 0.002129 | 15.85 | 221.5 | 0.027658 | 279.27 | 635.8 | 0.091433
16MB | 0.15 | 4.27 | 0.002116 | 16.19 | 176.18 | 0.027027 | 294.68 | 644.48 | 0.086973
64MB | 0.15 | 4.36 | 0.002137 | 17.83 | 238.83 | 0.027488 | 281.28 | 642.91 | 0.086046
256MB | 0.15 | 19.07 | 0.002112 | 18.82 | 912.81 | 0.027972 | 292.88 | 2448.83 | 0.086941

## Slide 15: Allgather, one datacenter, different sub chunk number
Unit: | NDv2, 1 chassis |  |  |  | NDv2, 2 chassis |  |  |  | NDv2, 3 chassis |  |  | 
 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8
1MB | 78.825 | 59.29375 | 49.528125 | 49.528125 | 686.29375 | 656.996875 | 642.3484375 | 635.02421875 | 1390.71875 | 1322.359375 | 1288.1796875 | 1271.08984375
4MB | 313.2 | 235.075 | 196.0125 | 196.0125 | 2737.075 | 2619.8875 | 2561.29375 | 2531.996875 | 5550.875 | 5277.4375 | 5140.71875 | 5072.359375
16MB | 1250.7 | 938.2 | 781.95 | 781.95 | 10940.2 | 10471.45 | 10237.075 | 10119.8875 | 22191.5 | 21097.75 | 20550.875 | 20277.4375
64MB | 5000.7 | 3750.7 | 3125.7 | 3125.7 | 43752.7 | 41877.7 | 40940.2 | 40471.45 | 88754 | 84379 | 82191.5 | 81097.75
256MB | 20000.7 | 15000.7 | 12500.7 | 12500.7 | 175002.7 | 167502.7 | 163752.7 | 161877.7 | 355004 | 337504 | 328754 | 324379
 | NDv2, 1 chassis |  |  |  | NDv2, 2 chassis |  |  |  | NDv2, 3 chassis |  |  | 
 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8
1MB | 78.825 | 59.29375 | 49.528125 | 49.528125 | 686.29375 | 656.996875 | 642.3484375 | 635.02421875 | 1390.71875 | 1322.359375 | 1288.1796875 | 1271.08984375
4MB | 313.2 | 235.075 | 196.0125 | 196.0125 | 2737.075 | 2619.8875 | 2561.29375 | 2531.996875 | 5550.875 | 5277.4375 | 5140.71875 | 5072.359375
16MB | 1250.7 | 938.2 | 781.95 | 781.95 | 10940.2 | 10471.45 | 10237.075 | 10119.8875 | 22191.5 | 21097.75 | 20550.875 | 20277.4375
64MB | 5000.7 | 3750.7 | 3125.7 | 3125.7 | 43752.7 | 41877.7 | 40940.2 | 40471.45 | 88754 | 84379 | 82191.5 | 81097.75
256MB | 20000.7 | 15000.7 | 12500.7 | 12500.7 | 175002.7 | 167502.7 | 163752.7 | 161877.7 | 355004 | 337504 | 328754 | 324379
Unit: | NDv2, 1 chassis |  |  |  | NDv2, 2 chassis |  |  |  | NDv2, 3 chassis |  |  | 
 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8
1MB | 0.002290 | 0.003761 | 0.007915 | 0.025631 | 0.027781 | 0.065134 | 0.161837 | 0.458582 | 0.085879 | 0.201244 | 0.533732 | 1.606632
4MB | 0.002129 | 0.003775 | 0.008128 | 0.025354 | 0.027658 | 0.065649 | 0.157466 | 0.457438 | 0.091433 | 0.207036 | 0.535467 | 1.593777
16MB | 0.002116 | 0.003892 | 0.008062 | 0.026154 | 0.027027 | 0.064883 | 0.157747 | 0.459048 | 0.086973 | 0.205340 | 0.536004 | 1.598344
64MB | 0.002137 | 0.003866 | 0.00829 | 0.025639 | 0.027488 | 0.065633 | 0.158043 | 0.458925 | 0.086046 | 0.206630 | 0.534120 | 1.590079
256MB | 0.002112 | 0.003942 | 0.007693 | 0.026302 | 0.027972 | 0.064795 | 0.159193 | 0.454419 | 0.086941 | 0.205294 | 0.533926 | 1.580135
 | NDv2, 1 chassis |  |  |  | NDv2, 2 chassis |  |  |  | NDv2, 3 chassis |  |  | 
 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8 | 1 | 2 | 4 | 8
1MB | 0.002290 | 0.003761 | 0.007915 | 0.025631 | 0.027781 | 0.065134 | 0.161837 | 0.458582 | 0.085879 | 0.201244 | 0.533732 | 1.606632
4MB | 0.002129 | 0.003775 | 0.008128 | 0.025354 | 0.027658 | 0.065649 | 0.157466 | 0.457438 | 0.091433 | 0.207036 | 0.535467 | 1.593777
16MB | 0.002116 | 0.003892 | 0.008062 | 0.026154 | 0.027027 | 0.064883 | 0.157747 | 0.459048 | 0.086973 | 0.205340 | 0.536004 | 1.598344
64MB | 0.002137 | 0.003866 | 0.00829 | 0.025639 | 0.027488 | 0.065633 | 0.158043 | 0.458925 | 0.086046 | 0.206630 | 0.534120 | 1.590079
256MB | 0.002112 | 0.003942 | 0.007693 | 0.026302 | 0.027972 | 0.064795 | 0.159193 | 0.454419 | 0.086941 | 0.205294 | 0.533926 | 1.580135
Collective time
Execution time
As the number of chunks increases, the collective time decreases, while the execution time increases.

## Slide 16: Thank you!